## Slide 1
Twomes
50 shades of green, from
4 white measurement devices, and
1 inverse grey-boxmodel?
Henri ter Hofte, h.ter.hofte@windesheim.nl
Associate Lector Energy Transition
transmission infiltration ventilation
heating
solar irradiation
‘internal’ heat
heat loss
heat gain

## Slide 2: Digital twins for the heating transition: 50 shades of green, from 4 white measurement devices, and 1 inverse grey-boxmodel?
Authors: Henri ter Hofte, Hossein Rahmani
Publication date: 24-05-2022
Parties involved: Research group Energy Transition (Windesheim)
Chair: Jeike Wallinga
Twomes Deliverable D8
This work is financially supported by BDR Thermea, Breman, Enpuls, TechForFuture, Witteveen + Bos and the municipality of Zwolle.
This is a publication by Saxion, University of Twente and Windesheim University of Applied Sciences
Licence: CC BY 4.0, Research group Energy Transition, Windesheim University of Applied Sciences
Notes: The results of project Twomes are described in the following deliverables:
Deliverable D1a Project Plan contains the project plan that forms the basis for research activities.
Deliverable D1b Data management plan describes what data is collected in the project, how data should be handled during the project and after the project is finished.
Deliverable D1c: Uitkomsten bewonersonderzoek describes (in Dutch) the results of the research we conducted into questions residents have about the heat transition, via surveys and/or interviews. We used insights gained to focus further research in the project lays the foundation for advice modules.
Deliverable D2: Dataset 1 contains the monitoring data that we collected for exploratory analysis.
Deliverable D3: Analysis Methods and Tools, Version 1 contains a description of the analysis methods and tools used to analyze data from Deliverable D2. We also describe what we can learn from the available data and what additional measurements we deem necessary.
Deliverable D4: Testable Hypotheses describes the hypotheses we want to test with the research in Twomes.
Deliverable D5: Measurement methods and techniques describes the (additional) measurement methods and techniques that we have developed to collect data used to test hypotheses from D4.
Deliverable D6: Subject Information, Consent Forms includes all information and documents (in Dutch) we use to recruit and educate subjects, including a description of how we obtain consent to collect data.
Deliverable D7: Dataset 2 contains the data that we collected to do a detailed analysis including research into the hypotheses of D4.
Deliverable D8: Analysis Methods and Tools describes not only the analysis methods and tools we applied to the dataset from D7, but also the results and conclusions of this analysis.
Deliverable D9: Dissemination and design follow-up research includes all external presentations and publications for interested parties outside the project, including a plan for a follow-up study for the realization of advice modules.
Deliverable D10: Presentations, Report, Update Plan and Schedule includes all interim and progress presentations of the project, and updated plans.

## Slide 3: In short
Twomes: Digital Twins for the Home Heating Transition
Crucial parameters for the heating transition of a specific home:
  Building: specific heat loss: H [W/K], thermal inertia: τ [s], apparent window area: A [m2]
  Installation: boiler efficiency η [%]
  Comfort: weekly home/away/asleep thermostat setpoints: <Tset;d;h> [Ks]
2-4 measurement devices (50-€100) per home to collect > 2 wk data
  smart meter monitor, room monitor, boiler monitor, OpenTherm monitor, app;
  available as open source software & open hardware designs on GitHub
  security, privacy & technical variety: more challenging than expected, but doable
  35 million datapoints from 23 homes in one heating season
Using the Twomes inverse grey-box model based on GEKKO Python:
  Building parameters H [W/K], τ [s] seem learnable; working on A [m2]
  More challenging than we expected!
  No time left in project to analyze boiler efficiency η [%]

## Slide 4: Who?
Twomes: Digital Twins for the Home Heating Transition
50 Tinten Groen Assendorp
  58 respondents on survey
  40 subjects invited to measure data at home
  3 installation helpers + primary contact
8 project partners
Windesheim
  36 students
    30 HBO-ICT
    6 Electrical Engineering
  10 teachers
  10 teacher-researchers
  1 project leader
  1 professor

## Slide 5
Francois Mori/AP
Why?
Notes: https://www.npr.org/sections/thetwo-way/2015/12/12/459502597/2-degrees-100-billion-the-world-climate-agreement-by-the-numbers?t=1599027444292

## Slide 6: hich home heating model parameters of specific homes can we learn automatically from energy monitoring data in order provide better advice to a specific household about their home heating transition?

## Slide 7: Which kind of questions should Twomes help answer?
Goal
Questions about all homes in a country
Questions about all homes in a city or neighbourhood
Questions that require close personal contact to answer
Questions about specific homes and households
Questions that can be answered with help of monitoring data

## Slide 8: ill our home be comfortable enough if we switch to a (hybrid) heat pump?

## Slide 9: Model parameters we want to learn
symbol | scope | parameter | unit
H | building | specific heat loss | W/K
τ | building | thermal inertia | s (or h)
C | building | thermal mass (C = H  τ) | J/K (or Wh/K)
A | building | apparent window area (imaginary horizontal window in roof) | m2
Pmax | installation | maximum heating system power (boiler + distribution) | W
ηs;CH | installation | central heating system efficiency (superior value) | %
<Tset;h;d> | comfort needs | weekly thermostat setpoints (home/away/asleep) | K‧s
Twomes WP3: Data Analysis & Prediction

## Slide 10: Model parameters for simulation
time series output data
Twomes WP3: Data Analysis & Prediction
indoor temperature
energy use
setpoint changes
weather
building
installation
comfort needs
time series input data

## Slide 11: Model parameters for simulation
Twomes WP3: Data Analysis & Prediction
indoor temperature
energy use
setpoint changes
weather
time series output data
time series input data
building
installation
comf.needs
model parameters (time-independent)

## Slide 12: Learn model parameters? Inverse grey-box modelling!
calculated data (time series data)
calculated output data (time series data)
Twomes WP3: Data Analysis & Prediction
indoor temperature
energy use
setpoint changes
weather
calculated data (time series data)
measured input data (time series data)
building
installation
comf.needs
model parameters (time-independent)
indoor temperature
energy use
measured comparison data (time series data)
?
calculated data (time series data)
calculated data (time series data)
calculated data (time series data)
calculated data (time series data)
calculated data (time series data)
calculated data (time series data)
calculated data (time series data)
calculated data (time series data)
calculated data (time series data)
calculated data (time series data)

## Slide 13: Predict how changed parameters change outcome
Twomes WP3: Data Analysis & Prediction
indoor temperature
energy use
setpoint changes
weather
calculated data
time series data
building
installation
comf.needs
model parameters (time-independent)
Notes: Thermostat setpoints can be e.g. replayed from a previous year, or derived from comfort needs. This depends on the type of prediction and comparison desired. Similarly, weather data can be e.g. replayed from a prvious year, or derived from a pre-determind average, also known as a ‘reference climate year’. Again, this depends on the type of prediction and comparison desired.

## Slide 14: Architecture
Twomes WP2: Data collection
smart meter
boiler
Enexis (DSO)
Twomes
Backoffice
OpenTherm Monitor
WiFi router
Internet
Enelogic (ODA)
Ts + Tr
smart meter module
Tin
P4
weather data
P3
open data about buildings (BAG, AHN, energy labels)
Twomes
Analysis pipeline
app
occupant
advisor

## Slide 15: Recruitment: variety in smart meters
Twomes WP2: Data collection
6 brands
13 models
3 versions DSMR standard
P1-poort: 9 in use; 31 not

## Slide 16: Recruitment: variety in thermostats
Twomes WP2: Data collection
10 brands / 25 models

## Slide 17: Recruitment: variety in boilers (+thermostats)
Twomes WP2: Data collection
boiler: 6 brands / 10 models
OpenTherm compatible: 27 yes / 13 no
boiler-thermostat-combis: 17 brand-brand 35 model-model

## Slide 18: Device preparation
Twomes WP2: Data collection

## Slide 19: Device deployment
Twomes WP2: Data collection

## Slide 20: Device deployment: 04-jan-22
Twomes WP2: Data collection
Status | # homes | # step loss | step success % | remaining %
Invited | 40 |  |  | 100 %
did not end participation | 37 | 3 | 93 % | 93 %
app activated | 32 | 5 | 86 % | 80 %
 1 device activated | 24 | 8 | 75 % | 60 %
all devices activated | 20 | 4 | 83 % | 50 %
 1 data source ok | 19 | 1 | 95 % | 48 %
all data sources ok | 8 | 11 | 42 % | 20 %
all data sources still ok | 4 | 4 | 50 % | 10 %

## Slide 21: Device deployment; follow-up
Twomes WP2: Data collection

## Slide 22: Data collection & pre-processing
Twomes WP2: Data collection
23 homes with >3 wk essential data
> 35 million data points
35% sane
4,5 y sane measurements (~ 70 d/home)

## Slide 23: Model: heat balance in interval
‘internal’ heat
solar irradiation
heating system (boiler + distribution)
WP3 Data Analysis & Prediction
occupants, electric appliances, domestic hot water (dhw)
heat loss: ΔQloss [J]
heat gain: ΔQgain [J]
temperature drop
transmission + infiltration + ventilation
specific heat loss: H [W/K] effective heat demand: ΔS [K s] where ΔS = (Tin-Tout;eff) [K] Δt [s]

## Slide 24: Analysis model equations (GEKKO Python)
WP3: Data Analysis & Prediction

## Slide 25: Analysis: weather in Assendorp, Zwolle
WP3: Data Analysis & Prediction

## Slide 26: Analysis: weather in Assendorp, Zwolle
WP3: Data Analysis & Prediction

## Slide 27: Analysis: data fora single home single week
WP3: Data Analysis & Prediction

## Slide 28: Analysis results (example; Berkum data; 1 week)
WP3: Data Analysis & Prediction

## Slide 29: Model parameters we wanted to learn
symbol | scope | parameter | unit
H | building | specific heat loss | W/K
τ | building | thermal inertia | s (or h)
C | building | thermal mass (C = H  τ) | J/K
A | building | apparent window area (imaginary horizontal window in roof) | m2
Pmax | installation | maximum heating system power (boiler+distribution) | W
ηs;CH | installation | central heating system efficiency (superior value) | %
<Tset;h;d> | comfort needs | weekly thermostat setpoints (home/away/asleep) | Ks
Twomes WP3: Data Analysis & Prediction

## Slide 30: Learning H [W/K] (specific heat loss) A = 6,0 [m2] (assumed; not learnt)
WP3: Data Analysis & Prediction

## Slide 31: Learning  [h] (thermal inertia) A = 6,0 [m2] (assumed; not learnt)
WP3: Data Analysis & Prediction

## Slide 32: Combining H [W/K] &  [h] each week one dot A = 6,0 [m2] (assumed; not learnt)
WP3: Data Analysis & Prediction

## Slide 33: Combining H [W/K] &  [h]; multi-week average A = 6,0 [m2] (assumed; not learnt)
WP3: Data Analysis & Prediction

## Slide 34: Model parameters we wanted to learn
symbol | scope | parameter | unit
H | building | specific heat loss | W/K
τ | building | thermal inertia | s (or h)
C | building | thermal mass (C = H  τ) | J/K
A | building | apparent window area (imaginary horizontal window in roof) | m2
Pmax | installation | maximum heating system power (boiler+distribution) | W
ηs;CH | installation | central heating system efficiency (superior value) | %
<Tset;h;d> | comfort needs | weekly thermostat setpoints (home/away/asleep) | Ks
Twomes WP3: Data Analysis & Prediction

## Slide 35: Learning A [m2]  [h] (thermal inertia) / H [W/K] (specific heat loss) also learnt
WP3: Data Analysis & Prediction

## Slide 36: Learning H [W/K] (specific heat loss) A [m2] (apparent window area) &  [h] (thermal inertia) / H [W/K] (specific heat loss) also learnt
WP3: Data Analysis & Prediction

## Slide 37: Learning  [h] (thermal inertia) A [m2] (apparent window area) & H [W/K] (specific heat loss) also learnt
WP3: Data Analysis & Prediction

## Slide 38: Combining H [W/K] &  [h] each week one dot A [m2] (apparent window area) also learnt
WP3: Data Analysis & Prediction

## Slide 39: Combining H [W/K] &  [h]; multi-week average A [m2] (apparent window area) also learnt
WP3: Data Analysis & Prediction

## Slide 40: Conclusions
WP3: Data Analysis & Prediction
Data collection experience in practice: challenging!
  Home (installation)s are varied!
  Every step in installation counts! (Local help helps a lot)
Data analysis experience in practice: challenging!
  Big data; lots of preprocessing; run time learning ~0,5 hour per homeweek
What we achieved
  Data collection method & tools; 13 open source software & open hardware GitHub repos; WarmteWachter app
  Indications that some building parameters can be learned: specific heat loss H [W/K], thermal inertia τ [s]
  Work in progress: apparent window area: A [m2]
Project time ran out before we could:
  analyze boiler efficiency ηs [%]
  Compare: simulate based on learned parameters / parameters calculated from a.o. building year, floor area

## Slide 41: hich questions do you have?
transmission infiltration ventilation
heating
solar irradiation
‘internal’ heat
heat loss
heat gain

## Slide 42: ill not present this hidden slide and others after this one. Slides may be used to answer questions.

## Slide 43: In a nutshell; questions
Twomes: Digital Twins for the Home Heating Transition
What are crucial physical parameters for the home heating transition of a home?
Can we collect energy monitoring data for this with a few measurement devices?
Can we learn the crucial parameters per home automatically from ~ 2 weeks of measurement data?

## Slide 44: Agenda
Twomes: Digital Twins for the Home Heating Transition
Summary
Who?
Why?
How? (method & tools we developed)
  Data Collection (WP2)
  Data Analysis (WP3)
So? (results, conclusion)
Now what?

## Slide 45: Research Group Energy Transition, Windesheim University of Applied Sciences
practice
research
Electrical Engineering
Civil Engineering
HBO-ICT
Mechanical Engineering
education
Vertalingen checken

## Slide 49: We need to stop burning fossil fuels (gas) for home heating in the Netherlands within one generation! Meaning: switch to another energy source
80% of homes in 2050 already built now
Challenge: many homes (Klimaatakkoord, 2019)
  2020 - 2030: 1,5 million homes in NL (> 600 homes per average working day)
  2030 - 2050: 5,5 million homes in NL (> 1100 homes per average working day)
Options:
  (hybrid) heat pump / district heating / biogas / biomass / hydrogen / infrared
  NB Energy source MUST be CO2-neutral within one generation!
Why?

## Slide 50: Some interventions to reduce home heating CO2-emissions
Building interventions isolation, crack sealing, HR++ glass, …
Installation interventions
  Installation: hardware high efficiency boiler, heat recovery, (hybrid) heat pump, district heating, biogas, biomass, hydrogen, infrared,…
  Installation: settings night setback, day setback, hydronic balancing, supply temperature, …
Comfort interventions warm clothing?, get used to lower temperatures?, …
Weather climate change?
Introduction
Notes: Since space in diagrams is limited; I switched to collapsing instatataion hardware interventions and installation settings interventions into one category. In subsequent slides, this allows for model parameter categories to be collapsed in to ‘installation parameters’.
Installation settings, however are often much easier to change than installation hardware. For example, changing the supply temperature of a gas-fired boiler is much easier than changing the gas-fired boiler for a heat pump (which often also implies changing the hydronic heat distribution system and sometimes even requires changing heat distribution of the the building envelope.

## Slide 51: elke bepalende parameters voor de warmtetransitie van specifieke woningen kunnen we leren met monitoringdata en welke vragen van huishoudens kunnen we daarmee beantwoorden?

## Slide 52: at kunnen we besparen met isolatie en/of het dichten van kieren van onze woning?

## Slide 53: at kunnen we besparen met betere instellingen van onze verwarming?

## Slide 54: Intro
Twomes: Digital Twins for the Home Heating Transition

## Slide 55: Energy monitoring data we collect
category | measured data | symbol | unit | API | sensor
comfort | setpoint | Tset | °C |  | 
weather | outdoor temperature | Tout | °C | (KNMI) | 
 | wind | W | m/s |  | 
 | global horizontal irradiation | I | W/m2 |  | 
indoor | indoor temperature | Tin | °C |  | 
installation | supply temperature | Ts | °C |  | 
 | return temperature | Tr | °C |  | 
energy use for heating | electricity | E | kWh |  (Enelogic) | 
 | gas | G | m3 |  | 
occupancy/ventilation | CO₂ concentration | CO₂ | ppm |  | 
 | Bluetooth presence | BTpres | #pp |  | 
Twomes WP2: Data collection

## Slide 56: Measurement devices we designed & made
Twomes WP2: Data collection
Device | Module | Cost incl. PCB, enclosure, power supply, cale | QR | Package A | Package B | Package C | Package D
OpenTherm monitor | OpenTherm monitor | € 25 |  |  |  |  | 
smart meter module | smart meter module | € 15 |  |  |  |  | 
smart meter module + boiler module + room monitor | smart meter module | € 15 |  |  |  |  | 
 | boiler module | € 25 |  |  |  |  | 
 | room monitor | € 20 |  |  |  |  | 
 | … with CO₂-sensor | € 50 |  |  |  |  | 
Total per home |  |  |  | € 40 | € 60 | € 115 | € 85

## Slide 57: Open Source and Open Hardware
Twomes WP2: Data collection
GitHub Research Group Energy Transition
  https://github.com/energietransitie/
Twomes Warmtewachter App
  twomes-app-warmtewachter
  esp-provisioning-capacitor-plugin
Twomes Server
  twomes-backoffice-api
  twomes-backoffice-configuration
Twomes Measurement Devices: Firmware
  twomes-generic-esp-firmware
  twomes-opentherm-monitor-firmware
  twomes-p1-gateway-firmware
  twomes-boiler-monitor-firmware
  twomes-room-monitor-firmware
Twomes Measurement Devices: Hardware
  twomes-opentherm-monitor-hardware
  twomes-p1-gateway-hardware
  twomes-temp-monitor-hardware
  twomes-co2-meter-hardware

## Slide 58: Measurement device software stack
Twomes WP2: Data collection
Bluetooth
Twomes Provisioning
Wi-Fi
ESP32
ESP8266
ESP-IDF
Unified Provisioning
heartbeat
secure upload
time syncing (NTP)
persistent buffering
presence detection
CO2 measurements

## Slide 59: Firmware data flow
Twomes WP2: Data collection
Secure Upload
Twomes generic firmware
other measure-ments
other measure-ments
2.4 GHz radio (IEEE 802.11/BLE)
Heartbeat
Time Syncing
Presence Detection
SEK-SCD41
incoming measurements from satellites
Twomes device-specific firmware
Twomes Provisioning
NTP > Wi-Fi
POST /device/measurements/
TLS/SSL > Wi-Fi
proprietary > ESP-NOW
POST /device/activate
TLS/SSL > Wi-Fi
toJSON(property,value)
toJSON(property,value)
queue
format
send
Persistent Buffering (spiffs)
toJSON()
toJSON()
RTC BM8563
NTP sync timer
heartbeat timer
presence timer
upload timer
other timer(s)
Wireless Resource Protection (FreeRTOS semaphore/mutex?)
ESP-IDF

## Slide 60: Deployment: 26-jan-22 (+3 wk)
Twomes WP2: Data collection
Status | # homes | # step loss | step success % | remaining %
Invited | 40 |  |  | 100 %
did not end participation | (+1 =) 38 | 2 | 95 % | 95 %
app activated | (+3 =) 35 | 5 | 92 % | 88 %
 1 device activated | (+3 =) 32 | 8 | 91 % | 80 %
all devices activated | (+10 =) 30 | 4 | 94 % | 75 %
 1 data source ok | (+9 =) 28 | 1 | 93 % | 70 %
all data sources ok | (+10 =) 18 | 11 | 64 % | 45 %
all data sources still ok | (+14 =) 18 | 4 | 100 % | (+35 % =) 45 %

## Slide 61: Deployment: 21-apr-22 (+15 wk)
Twomes WP2: Data collection
Status | # homes | # step loss | step success % | remaining %
Invited | 40 |  |  | 100 %
did not end participation | (+1 =) 39 | 1 | 98 % | 98 %
app activated | (+1=) 36 | 3 | 92 % | 90 %
 1 device activated | (+1=) 33 | 3 | 92 % | 83 %
all devices activated | (+3=) 32 | 1 | 97 % | 80 %
 1 data source >3wk ok | (+1=) 29 | 3 | 91 % | 73 %
Essential data >3wk ok | 23 | 6 | 79 % | 58 %
All data sources >3wk ok | 15 | 8 | 65 % | 38 %

## Slide 62: Heat balance
‘internal’ heat
solar irradiation
heating system (boiler + distribution)
Twomes Data Analysis & Prediction
occupants, electric appliances, domestic hot water (dhw)
specific heat loss: H [W/K] effective heat demand: ΔS [K s] where ΔS = (Tin-Tout;eff) [K] Δt [s]
heat loss: ΔQloss [J]
heat gain: ΔQgain [J]
Σ( Δt) [J/m2] A [m2] where average solar irradiation: It [W/m2]
gas for heating: ΔGCH [Nm3] superior calorific value gas:
upper net heating system efficiency, ηhs;CH [%]
temperature drop
electricity for heating: ΔECH [kWh] conversion factor from kWh to J:
Coefficient Of Performance, COPCH [-]
transmission + infiltration + ventilation
Notes: Model paramters are formatted in green
Time series data is has a subscript t; e.g. Tin;t is Tin (the average indoor temperature) at time interval t. Time intervals last a duration Δt.
N.B. This is the most simple building model; the effect of wind (a factor in infiltration) and changes in ventilation behaviour are modelled via effective outdoor temperature (Tout;eff;t), where accurding to KNMI research, the best simple approsimation is Tout;eff;t [°C] = Tout;eff;t – 2/3* ut [m/s], where ut is the average wind speed during time interval t. In more refines models, we will try to sepeara the influence of wind on the home heat los as a separate model parameter that is to be learned.

## Slide 63: Heat balance
or
where
is the thermal inertia
is the thermal mass
is the specific heat loss
of a particular home
transmission + infiltration + ventilation
Twomes Data Analysis & Prediction
temperature drop
or
where
is the thermal inertia
is the thermal mass
is the specific heat loss
of a particular home
ΔS = (Tin-Tout;eff) [K] Δt [s]
specific heat loss: H [W/K] effective heat demand: ΔS [K s] where ΔS = (Tin-Tout;eff) [K] Δt [s]
heat loss, ΔQloss [J]

## Slide 64: Occupancy, ventilation & CO2 concentration
Twomes
occupancy
ventilation
CO2 concentration
CO2 icons created by Freepik - Flaticon
Bluetooth
Passive InfraRed (PIR)
CO2 sensor (SDC41)
Electricity use
Heat loss
And hence also (simplified)
occupancy – CO2 concentration = ventilation (~ heat loss)
CO2 concentration – ventilation = occupancy

## Slide 65: Color coding legend
Tools, equipment
Existing homes/equipment/databases (blue)
  Boiler, thermostat, smart meter, Wi-Fi, app, KNMI, …
Data acquisition tools
  Measurement devices, WarmteWachter
Analysis
  Twomes analysis model, GEKKO code
Data
Fixed model parameters (blue)
  population averages, constant in time horizon
Measured input data (pink)
  case-specific, varying in time horizon
Model parameters (green)
  case-specific, constant in time horizon
Twomes

## Slide 66: Some model equations (see also Twomes D3)
, the indoor temperature change
, the heat loss
is the specific heat loss, a building model parameter
, the effective temperature difference
, the indoor temperature, measured via an indoor temperature sensor
, the effective outdoor temperature
, the geospatially interpolated outdoor temperature, calculated from measured wheather data from the KNMI API
, the geospatially interpolated wind speed, calculated from measured wheather data from the KNMI API
, the effective thermal inertia, a building model parameter
, the effective heat capacity of the home, a building model parameter derived from two others
Twomes WP3: Data Analysis & Prediction

## Slide 67: Berkum: Learning H [W/K] (specific heat loss) A = 6,0 [m2]
WP3: Data Analysis & Prediction

## Slide 68: Berkum: Learning  [h] (thermal inertia) A = 6,0 [m2]
WP3: Data Analysis & Prediction

## Slide 69: Berkum: Learning A [m2] (window aperture)
WP3: Data Analysis & Prediction

## Slide 70: Berkum: Learning H [W/K] together with  [h] & A [m2]
WP3: Data Analysis & Prediction

## Slide 71: Berkum: Learning  [h] together with H [W/K] and A [m2]
WP3: Data Analysis & Prediction

## Slide 72: Now what? Possible follow-ups
Twomes: Digital Twins for the Home Heating Transition
Analyse boiler efficiency
Intervention research (before-after), bv.:
  lower supply temperature (“Zet ‘m op 60”), hydronic balancing, isolation
Energy label based on practice
  Buildings (based on H [W/K],  [h], A [m2])
  Instalations ηupper;CH [%]: COPCH [-] (~ ENERGY STAR label Connected Thermostat? USA norm uses data from practice!)
  Comfort need: <Tset;h;d> [Ks]
Separate ventilaton losses obv based on presence & CO₂-concentratiion measurement
Smart control of hybrid heat pumps.
  learn ηs;CH [%], Pmax;cv [W], COPCH [-], Pmax;HP [W], H [W/K],  [h], A [m2], <Tset;h;d> [Ks]
  Weather prediction

## Slide 73: Possible scale-ups
Twomes: Digital Twins for the Home Heating Transition
Winter ’21-’22
  20 – 40 homes in Assendorp, Zwolle
2022
  Brains4Buildings: quantify flexibility
Winter ’22-’23
  100 – 200 homes?
Winter ’23-’24
  1000 – 2000 homes